## Slide 1: IIT – Introduction to Laser Safety

## Slide 2: Introductory Laser Safety
This course is designed to provide an introduction to safe laser work. It does not cover any single specific laser system or experimental design at IIT. Speak with your PI to discuss the specific safety of your experimental system

## Slide 3: Course outline
Fundamental Laser and Laser Safety Terminology
Laser Classifications
Laser effects on eye and skin
Non-beam hazards
Control measures

## Slide 4
Fundamental Laser and Laser Safety Terminology

## Slide 5
1: Gain Medium
2. Laser Pump energy
3. High reflectance coupler (“totally reflecting”)
4. Output coupler/partially reflecting mirror
5. Beam

## Slide 6: Basic Laser Terminology
Radiant Energy, Q (unit: J)
Radiant Power, Φ (unit: W)
Radiant Exposure or Energy Density, H, (Pulsed laser, unit: J/cm2)
Irradiance or Power Density, E, (CW laser, unit: W/cm2)

## Slide 7
Specular (mirror-like) reflections
Diffuse reflections
  Size and orientations of surface irregularities determine the type of reflection
  Specular: Irregularities < λincident
  Diffuse: Irregularities > λincident , randomly oriented
Scattering

## Slide 8
Absorption: transferring radiant energy to another form (heat)
Divergence: Angular spread of the beam over a distance (unit: milliradian)

## Slide 9
Range | Wavelength | Range | Wavelength
UVC | 100-280 nm | IRA | 780-1400 nm
UVB | 280-315 nm | IRB | 1400-3000 nm
UVA | 315-400 nm | IRC | 3000nm – 1 mm
VISIBLE | 380-780 nm ANSI Defines as 400-700 nm |  | 

## Slide 10
Typical research lasers
  Excimer: UVA through UVC ranges
  Carbon dioxide: 9600/10600 nm (IRC)
  Nd:YAG: 1064 nm (typical, IRA)
  Dye lasers: Variable and typically visible

## Slide 11: Important laser safety terminology
Accessible Emission Limit (AEL)
  The maximum power (W) accessible to eye/skin
  Specific
    Wavelength range
    Exposure time
    Aperture
    Distance
  For  > 4µm it is power density (W/cm2)
  Used for laser classifications

## Slide 12
Aversion Response
  Any physical movement (eyelid closure, eye movement, head turn, etc.) to avoid an exposure to a noxious or visible bright light stimulant. Assumed to be 0.25 sec.
  Note that UV and IR sources will not have an aversion response!

## Slide 13
Laser Controlled Area (LCA)
  The laser use area where the occupancy and activity of those within is controlled and supervised.
Nominal Hazard Zone, NHZ
  The space within which the level of direct, reflected, or scattered radiation may exceed the applicable Maximum Permissible Exposure (MPE).
  Exposures outside the NHZ boundary are below the applicable MPE.

## Slide 14
Maximum Permissible Exposure, MPE
  The level of laser radiation to which an unprotected person may be exposed without adverse biological changes in the skin or eye.
Retinal hazard region
  Defined as 400 nm – 1400 nm

## Slide 15
Laser Classification

## Slide 16: Laser Classifications
Lasers are broadly classified by hazard: the potential to inflict injury to workers
  Particularly injury to eye and skin
Laser systems are classified – a Class 4 laser whose beam is completely enclosed while operating would be classified as a Class 1 system when operating.

## Slide 17
Classifications give consideration to:
  Wavelength
  Pulse rate (for pulsed lasers)
  Laser power (Peak power for pulsed lasers)
Generally speaking, end users will not classify lasers (except home-built ones)
  The LSO and PIs may work together to classify a laser system though.

## Slide 18
Class 1 Laser Systems
  MPE cannot be exceeded at any time when viewing with the naked eye or with any typical magnifying optics
  Fully enclosed beams are classified as Class 1 when operating
  Usually considered “safe” under normal operation

## Slide 19
Class 1M Laser Systems
  Think “M” for “Magnification”
  MPE may be exceeded if viewed through magnifying optics.
  Usually considered “safe” unless viewed with magnifying optics

## Slide 20
Class 2 Laser Systems
  Only visible (400-700 nm) lasers
  For CW lasers, power limited to 1mW
  Aversion reflex provides protection (0.25 s)
  Class 2M lasers - MPE may be exceeded if viewed through magnifying optics

## Slide 21
Class 3 Laser Systems
  Class 3R: Classification based on output
    For  < 400 nm or  > 700 nm, accessible output between 1x-5x Class 1 AEL
    For 400 nm <  < 700 nm (i.e. visible), accessible output must be less than 5x Class 2 AEL (e.g. <5 mW).
    This also defines the 3R AEL.

## Slide 22
Class 3B:
  Lasers operating < 400 nm or greater than 1400 nm and (1) can emit radiant power greater than 3R AEL but LESS THAN 0.5 W for T ≥ 0.25 sec or (2) cannot produce accessible radiant energy > 0.125 J with an exposure of T < 0.25 sec.
  Lasers operating between 400-1400 nm, classification is dependent on radiant power (or energy for pulsed lasers) and exposure time.

## Slide 23
Class 4 Laser Systems
  All other lasers that exceed 3B AELs.

## Slide 24
Laser Effects on Eye/Skin and
Non-beam hazards

## Slide 25: A little anatomy
By Artwork by Holly Fischer [CC BY 3.0 (http://creativecommons.org/licenses/by/3.0)], via Wikimedia Commons

## Slide 26
Damage is wavelength dependent
  UVA (315-400 nm)
    Damage to lens
    Delayed effect (sometimes years), cataracts
  UVB/UVC (100-315 nm)
    Damage to cornea
    “Welder’s flash”

## Slide 27
  Visible and Near IR (400-1400 nm)
    Light transmitted to retina with optical gain (~100,000)
    Irradiance of 1mW/cm2  100 W/cm2
    “Flash blindness” and retinal burns/lesions
  Far IR (1400 nm – 1mm)
    Damage to cornea
    Corneal burns

## Slide 28
Pulsed lasers present other ocular issues – pressure transients in eye (pulses < 1ms)
  Causes internal bleeding as well retinal damage

## Slide 29
Skin damage – thermal burns in tissue
  Skin layer penetration depends on wavelength and power
  Photosensitive?
    Some medications enhance photosensitivity

## Slide 30: Non-beam hazards
Electrical
  Homemade laser systems
  Uncovered electrical connections
  Improper grounding
  Mechanically defeated interlocks for maintenance

## Slide 31
Mechanical
  Compressed gas cylinders
  Noise issues with pulsed excimer lasers
  Fire hazards from Class 4 lasers (irradiance > 10 W/cm2 or power > 0.5 W)
  Explosions from high pressure arc lamps, filament lamps and capacitors

## Slide 32
Chemical
  Some laser dyes are carcinogenic
  Solvents are usually flammable
Laser generated air contaminants
  Some can be carcinogenic (examples: polycyclic aromatic hydrocarbons, fused silica, benzene)
  Toxicity

## Slide 33: Other non-beam hazards
Some components may produce X-rays (ionizing radiation)
RF hazards may be present in plasma tubes or Q-switched lasers
Ergonomic considerations

## Slide 34
Hazard Control

## Slide 35: Controlling laser hazards
Layered control scheme
  Engineered controls (“scientist-proof” controls)
  Administrative controls (“rules”)
  Personal protective equipment (PPE)

## Slide 36: Engineered controls
Prevent unnecessary exposure to beam hazards
  Key controls (and not leaving the keys in the laser!)
  Housing interlocks
  Door entry interlock
  Emergency stops (power or shutter)
  Curtains and warning signals/lights

## Slide 37: Administrative Controls
If engineered controls are impractical or unavailable
  Rules to limit access while laser is in use
  Examples:
    Curtain use to confine laser to NHZ
    Work rules around lasers (i.e. energized equipment rules, chemical work rules, etc.)
    Reducing laser power for aiming
    Chemical handling rules

## Slide 38: PPE
PPE includes
  Minimizing exposed skin area (long sleeves)
  Eye protection
    Goggles must match wavelength and power to provide protection
    Protection to less than MPE

## Slide 39
Goggle selection
  To get required Optical Density, need to know:
    Wavelength
    Power
    Exposure time

## Slide 40: Responsibilities
End users are responsible for:
  Complete required training (including specific training for their own laser systems)
  Wearing appropriate PPE
  Following SOPs
  Conducting operations in a safe manner

## Slide 41
Principal Investigators are responsible for:
  Supervising the safe use of lasers and ancillary equipment
  Registration of all Class 3 and 4 Lasers
  Notification to EHS of the intent to acquire or build an Class 3 or Class 4 laser

## Slide 42
  Creating and implementing SOPs
  Ensuring their lab staff (including support staff) are trained
  Meeting requirements on posting, access control, PPE and medical surveillance
  Reporting known or suspected laser injuries
  Procurement/moving requirements

## Slide 43: Conclusions
More information in the IIT Laser Safety Program